## Slide 1: Device Driver & Device Tree
KienLT9
This training materials are reused from multiple sources including FSOFT materials and Freescale training document, public document
Internal Used Only

## Slide 2: Agenda
Introduce Platform Driver model
  Platform Device
  Platform Driver
Device tree
  Overview
  Basic syntax
  Device binding
  Accessing DT Information
  Compile

## Slide 3: Introduce Platform Driver model
Provices a mechanism to notify the kernel of available hardware on board
Mechanism to add the devices to the device model of the kernel
Used for non-discoverable devices
Driver for the devices on the virtual “Platform” bus

## Slide 4: Introduce Platform Driver model
Platform Driver
  Set of operations done on the device
  Platform Device
  Information about the device
  Deemed to be connected to a virtual “platform bus”

## Slide 5: Introduce Platform Driver model
Platform Driver API
#include <linux/platform_device.h> struct platform_driver { int (*probe)(struct platform_device *); int (*remove)(struct platform_device *); void (*shutdown)(struct platform_device *); int (*suspend)(struct platform_device *, pm_message_t state); int (*resume)(struct platform_device *); struct device_driver driver; const struct platform_device_id *id_table; }; int platform_driver_register(struct platform_driver *driver); /* Or, for non hot-pluggable devices */ int platform_driver_probe(struct platform_driver *driver, int (*probe)(struct platform_device *)); void platform_driver_unregister(struct platform_driver *driver);

## Slide 6: Introduce Platform Driver model
  Platform Device API
#include <linux/platform_device.h> struct platform_device { const char *name; int id; struct device dev; u32 num_resources; struct resource *resource; const struct platform_device_id *id_entry; /* Others omitted */ }; int platform_device_register(struct platform_device *pdev); int platform_device_unregister(struct platform_device *pdev); struct resource *platform_get_resource(struct platform_device *pdev, unsigned int type, unsigned int n); struct resource *platform_get_resource_byname(struct platform_device *pdev, unsigned int type, const char *name); int platform_get_irq(struct platform_device *pdev, unsigned int n);

## Slide 7: Introduce Platform Driver model
Platform Device Driver sketup
  Init device
#include <linux/init.h> #include <linux/module.h> #include <linux/platform_device.h> #include <linux/device.h> #define DEVICE_NAME "my_device" static struct platform_device my_device = { .name = DEVICE_NAME, }; void __init my_device_init_pdata(void) { /* Register "my-platform-device" with the OS. */ platform_device_register(&my_device); }

## Slide 8: Introduce Platform Driver model
  Register deriver
static int __init my_driver_init_module(void) { int ret; my_device_init_pdata(); ret = platform_driver_probe(&my_driver, my_driver_probe); //return platform_driver_register(&ineda_femac_driver); return ret; } /* entry point for unloading the module */ static void __exit my_driver_cleanup_module(void) { platform_driver_unregister(&my_driver); // driver_unregister(&my_driver); } module_init(my_driver_init_module); module_exit(my_driver_cleanup_module);

## Slide 9: Introduce Platform Driver model
  Init Driver
static int my_driver_probe(struct platform_device *pdev) { printk(KERN_ALERT " %s\n", __FUNCTION__); return 0; } static int my_driver_remove(struct platform_device *pdev) { printk(KERN_ALERT " %s\n", __FUNCTION__); return 0; } static struct platform_driver my_driver = { .probe = my_driver_probe, .remove = my_driver_remove, .driver = { .name = DEVICE_NAME, .owner = THIS_MODULE, }, };

## Slide 10: Introduce Platform Driver model
  Init Driver
static int my_driver_probe(struct platform_device *pdev) { printk(KERN_ALERT " %s\n", __FUNCTION__); return 0; } static int my_driver_remove(struct platform_device *pdev) { printk(KERN_ALERT " %s\n", __FUNCTION__); return 0; } static struct platform_driver my_driver = { .probe = my_driver_probe, .remove = my_driver_remove, .driver = { .name = DEVICE_NAME, .owner = THIS_MODULE, }, };

## Slide 11: Device tree
A Device Tree is a hierarchical data structure that describes the collection of devices and interconnecting busses of a computer system.
Device Tree (DT) is language for describing hardware.
Simplest definition: A Data Structure

## Slide 12: Device tree
Represent hardware configuration
in hierarchical way.
- Each node is named
- Each node has exactly one parent node
- Each node has properties containing data

## Slide 13: Device tree
Basic Syntax
Notes: Each node in the device tree has a name according to the following convention:
name@unit-address
The name component specifies the name of the node
The unit-address component of the name is specific to the bus type on which the node sits.
-- unit-address must be unique
-- should match the first address specified in the reg property of the node.
Data type
<u32> -- A 32-bit integer in big-endian format .
Example: the 32-bit value 0x11223344 would be represented in memory as:
address 0x11
address+1 0x22
address+2 0x33
address+3 0x44
<u64> -- A 64-bit integer in big-endian format
Example: the 64-bit value 0x1122334455667788 would be represented as two cells as: <0x11223344 0x55667788>.
<string> -- Strings are printable and NULL-terminated
<phandle> -- Reference to another node in device tree
<stringlist> -- A list of <string> values concatenated together

## Slide 14: Device tree
Step to create new device tree
  Define a compatible string
  Use the standard properties as applicable for the new device.
  Use the conventions if the new device fits into one the ePAPR defined device classes.

## Slide 15: Device tree
TODO : Update new example

## Slide 16: Device tree
TODO : Update new example

## Slide 17: Device tree
Accessing DT Information
Bootstrap code uses DT
  Serial port type, location
  Host bridge setup
  finddevice(), getprop() calls used to retrieve information from the DT
The pointer to DT binary representation is passed in r3 to the Linux kernel
  Rich set of API calls to retrieve information from the DT (arch/powerpc/kernel/prom.c)
  Some API calls also included in arch/powerpc/kernel/prom_parse.c
  of_find_compatible_node(), find node based in token in “compatible” property
  of_get_property(), find property given node and property name
  of_find_node_by_type(), searched for node given “device_type” property
  of_translate_address(), translates address from DT to CPU physical address:
At run time the DT

## Slide 18: Device tree
TODO : Update new example

## Slide 19: Device tree
Compile

## Slide 20
Thank You!